## Slide 1: Worker register and inclusion criteria Management of Benzene & Mercury exposure offshore
Hans Thore Smedbold

## Slide 2: Content
Risk assessment
Exposure assessment
Worker register
Management of benzene and mercury exposure

## Slide 3: Risk assessment

## Slide 4: The risk asssessment framework and process (ISO 31000)

## Slide 5: Establish context
Retrospective
Prospective
Different contexts /
perspectives:
Medical (dose (exposure) – respons)
Regulatory Compliance
Worker protection (NOROG)
Backward Forward

## Slide 6: Regulatory Compliance
Qualitative Requirements
Occupational Exposure limits
Assessment strategy
Assessment criteria

## Slide 7: OELs Benzene (in ppm)
Country | 8-hour | STEL | 12-hour | Short term
N | 1.0 |  | 0.6 | 3
NL | 1.1 / 0.2 |  |  | 
UK | 1.0 |  |  | 
ACGIH | 0.5 | 2.5 |  | 
NIOSH | 0.1 | 1 |  | 
Neptune Energy | 0.2 | 2.5 | 0.12 | 2.5

## Slide 8: Context – requirements to our strategy
Compliance assessment (no day with exposure above the OEL) (EU chemical directive)
The average / long term exposure (worker register)

## Slide 9: Worker register and inclusion criteria

## Slide 10: Content
Background
How this is are implemented in Norway
Inclusion criteria
Is or can be exposed
Example of implementation

## Slide 11: It started with ILO
First required by ILO in 1974
First mentioned in Norway in 1978
In different EU directives
Different implementation in national regulations
Agents:
  Carcinogenic (1A and 1B),
  Mutagenic and lead substances
  Radiation
  Asbestos, and
  Biological agents (group 4 and 5)

## Slide 12: Examples of national implementations
Austria: Register of all worker handling agents subject to registration regardless of exposure.
Norway: Register all workers that are or can be exposed. Registered information shall contain information regarding exposure level.

## Slide 13: Norwegian Labour Inspectorate (NLI)
The employer shall establish a register of workers that are or can be exposed to agents subject to this regulation.
The regulation specifies which agents that is subject for the register.
Which information that shall be registered.
Who should have access to the register (VO, worker, HSE / OHS personnel, managers).
The retention / storage time of the register (> 60 years).
Inclusion in the register shall not take into account the effect of PPE
The register shall include information about the exposure level.
For later use of the information I will also recommend registration regarding use of PPE (as part of the exposure level description).

## Slide 14: Aim of the register (as stated by NLI)
For the company:
  Part of the systematic HSE work to control and improve the working condition
  Basis for risk based medical follow up of the worker
For the worker:
  Documentation of individual exposure
For the society:
  Research

## Slide 15: What is mend by being “exposed to”
Working with
Being in the vicinity of (access control + chemical index / storage chart)
Risk assessment (WEHRA)
Need to use respiratory protection (hours with respirators)
A fraction of the OEL (document exposure level)

## Slide 16: Is or can be exposed
«Is exposed»
«Can be exposed»
«Un-exposed»
Kari Normann:
Prosessoperatør Exposed
Kontrollromsoperatør Unexposed
Prosessingeniør land Unexposed
Yearly update

## Slide 17: Is or can be exposed
XXXXX (Norway):
One or more days a year with full shift exposure > 1/10 of the OEL

## Slide 18: Two ways into the register (JEM and OHS)
Jobb exposure matrix (JEM)
Worker register
Activity and process data (WO)
Exposure measurements (point samples and OH measurements)
Work Related Illnesses
Area charts (WEAC)
Risk assessments mm
HR - data
OHS
Feedbakck to worker being included into the register

## Slide 19: Risk assessment, cont.

## Slide 20: Annual population of exposures for one worker: 250 Worker-days per Year

## Slide 21: Hypothetical exposures for a Category 4 worker per year (OEL=1):

## Slide 22
What is an appropriate distributional model for describing the exposure profile?
  Lognormal ?
  Normal ?
  Something else ?

## Slide 23: Example of a possible «thrue» exposure profile
Null eksponering + lav eksponering
Sjelden høy fullskifts eksponering – knyttet til vedlikehold etc.
Unexposed days (30%),
Days with only tasks with short – high exposure (65%)
Days with long – high exposure (5 %)

## Slide 24: Exposure profile
95%il
0
0,002
0,004
0,006
0,008
0,01
0,012
0,014
0
50
100
150
200
250
300
Consentration
UTL
OEL
95%il = 95 prosentil
UTL = Upper Tolerance Limit
OEL = Occupational Exposure Limit

## Slide 25: Normal distribution
m-2s
m
m+2s
m-s
m+s
When the data fit the normal distribution, its known properties can be used
Area = 0.684
Area = 0.954
Notes: This is a picture of a normal distribution.
If you look at data within one standard deviation from the mean, note that the curve would cover 68.4% of the data.
If you look at data within two standard deviations from the mean, note that the curve would cover 95.4% of the data, leaving approx. 2.5% in each tail.
This information will be helpful when we are concerned about what percent of the data are less than a certain value, e.g. are in compliance.

## Slide 26: Special issues
Truncated data (what we didn't measure)
Censored data (values above or below the measurement range of your instrument)
Is there any true «null» exposed ?

## Slide 27: 2007-09 STAMI report 9/2011

## Slide 28: New assessment criteria (EN-689 (2018))
Minimum 3 “full shift” measurements
For small measurement series (3-5 measurements):
  N = 3 Maximum value less than 10% of limit value
  N = 4 Maximum value less than 15% of limit value
  N = 5 Maximum value less than 20% of limit value
For "medium sized" datasets (6-10 measurements):
  Check exposure profile (professional judgement). Assume log-normal if it cannot be proved otherwise. For values ​​of GSD (geometric standard deviation) > 3.5-4, evaluate whether the measurements can be grouped differently (see standard for identifying comparable exposed groups (SEG).
  x = measurement values
  Calculate: y = ln (x) for all measurements
  Calculate: average of y (y_bar) and standard deviation to y (sy)
  Calculate: GSD = exp (sy)
  Calculate X(0.95.0.70) = exp (y_bar + UT * sy), where UT (see table)
  Compare X (0.95,0.70) with OEL. If X(0.95.0.70) less OEL, the exposure may be considered to be below the limit, if equal or above the OEL the exposure is not considered to be in compliance with the regulations.
No samples | UT
6 | 2,18677
7 | 2,12007
8 | 2,072
9 | 2,035
10 | 2,005

## Slide 29: «New» assessment strategy
Must be aible to document exposure and absent of exposure «null» exposure. Use of activity log (log book).
Identify tasks with exposure (log book + VOC (PID)).
Fullshift measurement with dose badges (3M 3500 or ATD tubes).
Detailed exposure assessment related to identified exposed tasks (from A and B)) by Occupational Hygienist (source strength measurements + breathing zone measurements).

## Slide 30: Mapping of process streams
Closed system sampling
Head space analyses

## Slide 31: Worker protection regime (NOROG guideline 131)
Benzen applied as an indicator of health risk related to HC exposure
«Trigger value» for use of respirator protection - 0,05 ppm
(0,05 ppm level of detection (LOD) Dräger CMS)

## Slide 32: Comparison of the different perspectives
 | Medical * | Regulatory compliance * | Worker Protection NOROG
Criteria | 0.5 ppm (long term exposure) | 0.5 ppm (8-hour)* | 0.05 ppm (point sampling, often close to source)
Desition statistics | Aritmetisc mean, cumulative exposure | Geometric mean, 95-persentil, X(0.95.0.70) | Direct comparison with trigger value
What characterizes a deviation | Regular fullshift exposure with HC | Sporadically fullshift exposure > OEL | Sporadically task exposure > trigger value
Cumulative lifte time exposure (40 year with «acceptable» exposure) | 20 ppm*year | < 4.8-14 ppm*year | < 0.2 ppm*year
* ACGIH TLV for benzene

## Slide 33: Barrier requirements
Depends on selected perspektive og assessment method
A retrospective assessment compared to 20 ppm*year, or
Woker protection (NOROG 131) 0.05 ppm (spot sampling)

## Slide 34: Exposure influencing factors. EXAMPLE WIND
Wind speed (m/s) | Influence
< 2 | Lav
2-5 | Moderat
5-10 | Høy
>10 | Høy
80 % OF THE TIME > 5 m/s

## Slide 35: Laboratory worker Simulert (Monte Carlo) daglig eksponering

## Slide 36: Different assessments – different conclusions
Stilling |  | Frekvens | Varighet | Intensitet | M | R-8t | R-15m | B
Mekaniker | Inspeksjons av flowline | Ukentlig | 10 timer | Lav-Høy |  |  |  | 
 | Inspeksjon av syklon | Årlig | 10 timer | Lav-Høy |  |  |  | 
 | Inspeksjon av separatorer | 2-3 år (shutdown) | 2-3 timer | Lav-Høy |  |  |  | 
Prosessteknikker | Skifte filter på plateseparator | Ukentlig | 1 time | Lav |  |  |  | 
 | Prøvetaking av råolje | Hvert kvartal | 7-8 min | Lav |  |  |  | 
 | Prøvetaking av produsert vann | Daglig | 15 min | Lav |  |  |  | 
Laboratorie ing. | Prøvetaking | Daglig | 30 -160 min | Lav |  |  |  | 

## Slide 37: Manage benzene and mercury exposure offshore

## Slide 38: Mercury
In all oil and gas streems
Large variation between wells
Accumulates in all process equipment
Different forms
Hg - Metalic,
Sulfides and oxides
Organic mercury
Notes: Akutt eksponering:
Forgiftning som ligner metallfeber; frysninger, kvalme, dårlig allmenntilstand, brystsmerter, kortpustethet, hoste, betennelse i tannkjøttet.
Kronisk eksponering:
Permanent skade på hjerne eller nyrene kan være dødelig. Skader på sentralnervesystemet kan påvirke motorikk og kognitive evner (redusert konsentrasjon/hukommelse). Kan opphopes i kroppen.
Fosterskadelig

## Slide 39: Management of mercury in O&G
10-20 % Loss from well to export stream

## Slide 40: OEL Norway
OEL metalic Mercury
8 hour : 0,02 mg/m3 (20 µg/m3)
12 hours: 0,012 mg/m3 (12 µg/m3)
Short term : 0,06 mg/m 3 (60 µg/m3)
OBS!
1 mg = 1 000 µg = 1 000 000 ng

## Slide 42: Heating of a ”clean” gas pipe (stainless steel)

## Slide 43: SUMMARY
Production of oil and gas = benzene and mercury management
Mercury contamination of process equipment is only a matter of time
Lack of documentation - is not a proof of absence of exposure

## Slide 44: NOROG Worker Protection Regime

## Slide 45: Decision rules – how to manage the exposure
By area
By task
By exposure level
Exposure limit - knowledge – predictability – training – resources – equipment - PPE

## Slide 46: Assigned Protection Factor - respirator
The protection obtained of 95% of the users, 95% of the time.
Type of respirator | APF
Half mask with fixed filter (3M | 4
Half mask w/ combinasjon filter (ABEK1 Hg P3 R) | 10
Full maske w/ combination filter (ABEK1 Hg P3 R) | 20
Fan assisted respirator | 
Shield + combination filter (ABEK1 Hg P3 R) | 10
Full mask w/ combination filter (ABEK1 Hg P3 R) | 40
Fresh air supplied respirator | 
Half mask with constant air supply | 50
Full mask with constant air supply | 250
Half mask with demand air supply | 1000
Full mask with demand air supply | 1000
Full mask with demand air supply with over pressure | 2000
Under work

## Slide 47: Fit testing of respirator
Qualitative
Quantitative

## Slide 48: Type measuring equipment

## Slide 49: proactima.com
Prepared.